## Slide 1
IP Addressing

## Slide 2
Outline
IP Address Concepts
Private and Public Addresses
Network Address Translation (NAT)
Subnet Mask, Default Gateway
Domain Name Service (DNS)
Troubleshooting Network Connectivity

## Slide 4
IP Address Concepts
IP Address
  Identifier in IP layer of TCP/IP protocol suite to identify devices connected to the internet
  Unique
  Universal
Address Space – number of addresses used by the protocol
  E.g. the address space of 1Pv4 is 232 or 4,294,967 ,296.
Notation
  3 common notation for IPv4
    Binary (base 2)
    Dotted-decimal (base 256)
    Hexadecimal (base 16)

## Slide 5
IP Address Concepts
Internet Protocol (IP) Addresses
  Part of the TCP/IP Suite
Assigned to hosts (computers)
Unique in the network

## Slide 6
IPv4
IPv4 Address consists of a 32 bit number
  4 octets(8 bits) separated by space or dot
IPv4 Address examples in dotted-decimal notation
  172.20.1.5
  182.56.32.4
  8.8.8.8
Examples in Binary notation (base 2)
  10101100.00010100.00000001.00000101
  10110110.00111000.00100000.00000100
  00001000.00001000.00001000.00001000

## Slide 7
Binary Number System

## Slide 8
Binary to Decimal Conversion
Practice

## Slide 9
Binary to Decimal Conversion
Practice
Answer = 176
Answer = 255

## Slide 10
Binary to Decimal Conversion

## Slide 11
Decimal to Binary Conversion
168 = ? binary

## Slide 12
Decimal to Binary Conversion

## Slide 13
Subnet Mask
To define the network and host portions of an address, a devices use a separate 32-bit pattern called a subnet mask
The subnet mask does not actually contain the network or host portion of an IPv4 address, it just says where to look for these portions in a given IPv4 address

## Slide 14
Subnet Mask

## Slide 15
Default Gateway
Default Gateway
  Used to connect hosts to REMOTE networks
  Usually a router/firewall is a default gateway

## Slide 16
Public and Private IP Addresses
Private address blocks are:
Hosts that do not require access to the Internet can use private addresses
  10.0.0.0 to 10.255.255.255 (10.0.0.0/8)
  172.16.0.0 to 172.31.255.255 (172.16.0.0/12)
  192.168.0.0 to 192.168.255.255 (192.168.0.0/16)

## Slide 17
NAT and Private IP Addresses
Private addresses are NOT ROUTED to the internet
Network Address Translation (NAT) needed for internet access

## Slide 18
Domain Name Service
A human legible name is resolved to its numeric network device address by the DNS protocol.

## Slide 19
Domain Name Service
Utility called nslookup allows the user to manually query the name servers to resolve a given host name
Utility can be used to troubleshoot name resolution issues and to verify the current status of the name servers

## Slide 20
Test Connectivity - PING

## Slide 21
Test Connectivity - PING

## Slide 22
Test Connectivity - PING

## Slide 23
Test Connectivity - PING

## Slide 24
Test Path - Traceroute
  Traceroute
  Generates a list of hops that were successfully reached along the path.
  Provides important verification and troubleshooting information.

## Slide 25
Test Path - Traceroute
  Traceroute

## Slide 26
Summary
IP Address Concepts
  32 bits, Unique in the network
Private Addresses
    10.0.0.0/8
    172.16.0.0/12
    192.168.0.0/16
Network Address Translation (NAT)
Subnet Mask, Default Gateway
Domain Name Service (DNS)
  Resolves domain names to IP Addresses
Troubleshooting – ping, tracert